## Merge Recordings from CoCo80x + 90x
This document will detail steps to import and merge timestream recordings obtained simultaneously on the CoCo 80x and CoCo 90x.
- Connect a signal source / sensor to an input channel on the CoCo 80x and 90x.
- Ensure that GPS is turned on and the Status:Locked

- Ensure the Sampling Rate is the same between the two devices.
- Start Recording timestreams on both the CoCo devices.
- Ensure that there is overlap in time between the two-time stream recordings.
- Stop recording.
- Launch the Post Analyzer software.
- Choose Signal Analysis with Time Stamps as the project type. Choose option to Merge and Analyze Multiple Files:

Click to Add Files and Import the two recording files made on the CoCo80x and 90x and click OK to being process of merging recording files

Import the Merged file onto Signal Analysis with Time Stamps. Select APS and FRF.

To ensure the Merge operation is done accurately, check the FRF between the input channels connected to signal source on the CoCo devices. Ensure Phase ~ 0 [deg]

To Export the Merged Time Domain file, navigate to Source Files > Data Source > Right Click on the merged file and choose a suitable export format.