# Spectral Analysis
The Spectral Analysis page can be accessed by connecting to a Ruby via USB.

For more details on controlling the signal display traces, see Moving and Zooming around in the Signal Display Traces or Navigating Signal Display Controls.
## Spectral Analysis Parameters
Tap the Parameters button to open a menu that contains additional buttons for editing the spectral analysis settings. Sliding left on the menu will reveal more buttons.

### Sampling Rate
Change the sampling rate from 16.00kHz to 125.0Hz.
### Analysis Parameters
Change various analysis parameters such as:
- Block size
- Average mode
- Average number
- Window type
### Location ID
Change the location ID of each channel.
### Trigger Setup
Change the trigger setup of the signal from:
Free Run

Auto-Arm Trigger

### Record Setup
Change the signal recording of:
- Which channels to record
- How many points to record
  - Or how long of a duration to record for
## Spectral Analysis Controls
Tap the Control button to open a menu that contains additional buttons for controlling the spectral analysis traces.
- Restart: restart the spectral analysis data acquisition.
- Record: record signal data from the connected Ruby according to the current spectral analysis settings that will be stored in the Ruby.